## Slide 1
Engineering Mechanics I
Addis Ababa Science and Technology University
Animut.A

## Slide 2: 1.1 Introduction
Mechanics is an area of science concerned with the behavior of physical bodies when subjected to forces or displacement.
Translation
Rotation

## Slide 3: 1.1 Introduction
What is mechanics and its application Engineering science?
Mechanics is the physical science which deals with the effects of forces on objects. It is divided into three parts:
      mechanics of rigid bodies,
      mechanics of deformable bodies, and
      mechanics of fluids.
      Mechanics of rigid bodies includes
      Statics
      Dynamics
.
Notes: Good morning?
Today we will see, …
we will begin with brainstorming questions that such as:…
How could define …?
Why it is important to …?

## Slide 4: 1.2 Basic Concepts
The following definition and concepts are basic to the study of mechanics.
Space: geometric region occupied by bodies
Time: the measure of the succession of events
Mass: measure of inertia of a body. Mass can also be thought of as the quantity of matter in a body
Force: the action of one body on other. It tends to move a body in its direction of action
Particle: a body of negligible dimensions
Rigid body: a body is considered rigid when the change in distance between any two of its points is negligible.

## Slide 5: Fundamental Principles
The three laws of newton
First law: a particle remain at rest or continues to move in a straight line with a uniform velocity if there is no unbalanced force acting on it
Second law: the acceleration of a particle is proportional to the resultant force acting on it and its in the direction of this resultant force
Third law: the forces of action and reaction of interacting are equal in magnitude, opposite in direction and collinear

## Slide 6: 1.3 Scalars and Vectors
What is a Scalar quantities?
have only magnitude.
What is a Vector quantities ?
have both magnitude and direction

## Slide 7: Types of Vectors
Free Vectors:
(not confined or associated with a unique line)
Sliding Vectors:
have unique line in space

## Slide 8: Types of Vector
3) Fixed Vectors:
(unique and well-defined point of application)

## Slide 9: Classification of Vector
Based on coexistence of vector
Concurrent vector:- the line of action of the vector meet at one point.
concurrent non concurrent

## Slide 10: Classification of Vector
Collinear vectors:- all of the line of actions of them are parallel.
linear non linear
Coplanar vectors:- lines of action of the vectors lie on the same plane. Any two vectors are coplanar
Space vectors:-

## Slide 11: Representation of Vector
Graphical representation
Head
Tail
Length of the line segment

## Slide 12: Representation of Vector
B. Algebraic (Arithmetic) representation
represented by the components of the vector
z
y
x

## Slide 13: Properties of Vectors
Equality of vectors:
have the same magnitude and direction
The Negative of a vector:
equal magnitude but opposite in direction.
A
B
C
A
-A

## Slide 14: Properties of Vector
Null vector:
Unit vector

## Slide 15: 1.4 Operation With Vectors
Vector Addition or Composition
A. Graphical Method
B. Analytical Method

## Slide 16: 1.4 Operation With Vectors
A. Graphical Method
The parallelogram law

## Slide 17: 1.4 Operation With Vectors
II. The Triangle rule

## Slide 18: 1.4 Operation With Vectors
B. Analytic method
Trigonometric rules
applying the cosine and the sine rules.

## Slide 19: 1.4 Operation With Vectors
Trigonometric rules
From Cosine law
….. magnitude
From Sine law
…direction

## Slide 20: 1.4 Operation With Vectors
II. Component Method of Vector Addition

## Slide 21: 1.4 Operation With Vectors
Example
For vector V1 and V2 shown on the next slide
Determine the magnitude S of their vector sum S = V1+V2
Determine the angle between S and the positive x-axis.
Write S as a vector in terms off unit vectors i and j and then write a unit along the vector sum S.
Determine the vector difference D = V1 - V2

## Slide 22: 1.4 Operation With Vectors
Example cont..

## Slide 23: 1.4 Operation With Vectors
Solution
We construct to scale the parallelogram

## Slide 24: 1.4 Operation With Vectors
Solution
2. Using the law of sine for the lower triangle

## Slide 25: 1.4 Operation With Vectors
Solution
3. With knowledge of S and
Unit vector in the direction of S

## Slide 26: 1.4 Operation With Vectors
Solution
3. The vector difference D

## Slide 27: 1.4 Operation With Vectors
Vector Multiplication
1. Multiplication of vectors by scalars
2. Multiplication of vector by a vector
2.1 Dot Product: Scalar Product
2.2. Cross Product: Vector Product
1. Multiplication of vectors by scalars
Let n be a non-zero scalar and be a vector, then multiplying by n gives as a vector whose magnitude is and whose direction is in the direction of if n is positive or is in opposite direction to if n is negative.

## Slide 28: 1.4 Operation With Vectors
2. Multiplication of vector by a vector
2.1 Dot Product: Scalar Product
The scalar product of two vectors A and B which are  degrees inclined from each other denoted by A.B (A dot B) will result in a scalar of magnitude
i.e.
If analytically expressed
&

## Slide 29: 1.4 Operation With Vectors
2.2. Cross Product: Vector Product
AxB =
&

## Slide 30: Thank You